Sinth: A very simple digital synthesizer.

Docs for Version: 0.10 Dec 14 1995

Sinth is the backend to the internet synthesizer. It reads a control file
and produced a sound file. This control file sets up the connections
between the various software emulations of analog modules, and also
sets up the values for various "constant" parameters.
  In order to make some things simpler, a number of defaults are given so
everything need not be explicitly specified in all cases.

Syntax:
      sinth [-q] [control filename  or - for stdin]

Sinth is called with the name of a control file as a parameter (or '-' for 
stdin), and produces a sound file on stdout and a connection diagram on 
stderr. Using the -q option supresses the connection diagram.

for example:

sinth ex01.sinth > /tmp/t.au
     Sinth 0.10 Dec 14 1995
File Version 0.00  Sound Format: MuLaw  Sample Rate:8012
Duration:0.50  Trigger: On:0.33 Off:0.17 Rep: 0
             Plugboard
 c1  . . . . . . . . . . . . . . . . . 0.000000
 c2  . . . . . . . . . . . . . . . . . 0.000000
 c3  . . . . . . . . . . . . . . . . . 0.000000
 c4  . . . . . . . . . . . . . . . . . 0.000000
 c5  . . . . . . . . . . . . . . . . . 0.000000
 c6  . . . . . . . . . . . . . . . . . 0.000000
 c7  . . . . . . . . . . . . . . . . . 0.000000
 c8  . . . . . . . . . . . . . . . . . 0.000000
 c9  . . . . . . . . . . . . . . . . . 0.000000
c10  . . . . . . . . . . . . . . . . . 0.000000
 o1  . . . . . . . . . . . . . . . . * Sine Hertz
 o2  . . . . . . . . . . . . . . . . . Sine Hertz
 o3  . . . . . . . . . . . . . . . . . Sine Hertz
 n1  . . . . . . . . . . . . . . . . .
eg1  . . . . . . . . . . . . . . . . . 0.00  0.00 0.00  0.00 0.00  0.00 0.00
eg2  . . . . . . . . . . . . . . . . . 0.00  0.00 0.00  0.00 0.00  0.00 0.00
eg3  . . . . . . . . . . . . . . . . . 0.00  0.00 0.00  0.00 0.00  0.00 0.00
 f1  . . . . . . . . . . . . . . . . .
 g1  . . . . . . . . . . . . . . . . .
 g2  . . . . . . . . . . . . . . . . .
sq1  . . . . . . . . . . . . . . . . .
sq2  . . . . . . . . . . . . . . . . .
    +-----+-----+-----+---+---+-----+---+
    |F A D|F A D|F A D|S E|S E|S F Q|Out|
    | Osc1| Osc2| Osc3| G1| G2| F1  | 1 |
sq1: 0.00 0.00 0.00 0.00 0.00 0.00 0.00 0.00 
speed: 0.05
sq2: 0.00 0.00 0.00 0.00 0.00 0.00 0.00 0.00 
speed: 0.05

Operating:  o1

This chart shows information on the output format, its sample rate,
how long the sound is, the trigger parameters, the "connections" between
signals.  Sources are listed on the left, destinations on the bottom,
and an asterisk shows a connection. Values of parameters are shown on the
right.
For instance, here, O1  is plugged into the Output.
Oscillator 1 is a Sine wave, interpreting frequency info as Hertz
(aka cycles/second). 
At the bottom of the chart, a list of operating modules
is given. For optimization, only the modules which produce output 
are run!

         Description of Synthesizer Modules:

This synthesizer uses a number of modules, and each module processes a
number of inputs into a number of outputs. There are also some static
parameters, which are mostly switches and things you set once and
forget. How the signals get routed and the constants get set is
described in a control file. The basic syntax of each command
in the control file is:
 [destination] = [source] ;
 [parameter] = [floating point number or keyword] ;

The '=' is optional, and the ';' is as well, unless there are 
several commands on a single line. '#' will comment out the rest of
the line. All commands are case-insensitive and can have various
amounts of "white space" around the keywords. Sinth will catch most
if not all syntax errors and complain about them on stderr.

Very Important: the output of the synthesizer is taken from the
output of Out, so something had better be plugged into 
it in order to be heard!!

In the following descriptions, the dynamically changing parameters 
of a module are called "inputs", while the constant ones are called
"parameters." To specify which of several modules is being used, 
"n" in the parameter name is replaced with an identifying number, e.g.
"OnF" can be O1F, O2F or O3F (the frequency input for an oscillator).
   
   Oscillators: 
          
          Oscillators generally supply repeating signals which are used as
          sound sources. They can also provide signals which control other
          modules' characteristics. The frequency is a number given either
          in Hertz for an accurate frequency, or a real number from -3.0 to
          5.0 (roughly) which corresponds to the logorhythmic "1 unit per
          octave" standard, based on 0 representing a lowish frequency C.
          The amplitude scales the output and is usually connected to an
          envelope generator. The duty cycle warps the phase of the signal,
          which is only used in the square wave and triangle wave. Valid
          values for duty cycle are -1.0 (for 0%) to 0.0 (for 50%) to 1.0
          (for 100%) - so you can plug a unit-scaled signal directly into
          this parameter. Oscillators' signals can be plugged into each
          other to make Amplitude Modulated (AM) or Frequency Modulated
          (FM) sounds as well.
          
          + inputs: Freqency (OnF), Amplitude (OnA), Duty Cycle (OnD)
          + output: On
          + parameters: Waveform (OnW) [Square,Triangle,Saw_Up, Saw_Down
            or Sine],
            Frequency Scale (OnFS): log (1 unit/octave) or Hertz (linear)
            frequency.
            
          
   Noise:
          
          Noise is a random signal that sounds like static on the radio.
          But when filtered and mixed with other signals, it's quite
          useful. It can be treated as a random constant between -1.0
          and 1.0.
          
          + output: N1
            
   Envelope Generators:
          
          Envelope generators make commonly used control signals. The EG's
          themselves are controlled by a trigger signal. When the trigger
          starts, the value of the control starts changing from the Start
          Level toward the Attack Level at the Attack Rate. When that level
          is reached, it starts changing toward the Sustain Level at the
          Decay Rate. The signal remains at the Decay level until the
          trigger signal turns off, at which point the signal drops again
          to the Release Level at the Release Rate. All these rates
          are specified as "inverse seconds", i.e. a rate of 10 means
          the transition will take place in 1/10 of a second. The higher,
          the faster. 
                    
          + parameters:Start level (EnL),
            Attack rate (EnAR), Attack level (EnAL),
            Decay rate (EnDR), Sustain level (EnSL),
            Release rate(EnRR), Release level (EnRL)
          + output: EGn
            
   Sequencers: (called SQ1,SQ2)

          Sequencers provide a timed series of 8 control signals. The 
          speed that the sequencer runs at is controlled by a parameter 
          SQnS. The values can be used to make a very, very short melody.

          + parameters: Values (SQnA..SQnH),Speed (SQnS)
          + output: SQn
            
          
   Gates:
          
          Gates modulate the amplitude of an input signal with control
          signal, which is usually a signal from an envelope generator, but
          could be another Oscillator (for ring-modulator effects).
          
          + inputs: Signal(GnS),Envelope(GnE)
          + output: Gn
            
   Out:
          This is the output! (future: stereo, etc.)
          
          + inputs: OUT
          
   Low Pass Filter:
          
          A low pass filter is used to remove high frequencies - those
          below frequency "F" - from a signal. The resonance controls both
          how much the higher frequencies are attenuated and how much that
          frequency is boosted. When the Resonance is 1.0, the filter
          becomes a sine wave oscillator with the frequency of F!
          
          + inputs: Signal(F1S), Frequency (F1F), Resonance (F1Q)
          + output: F1
            
          
   Constants:(C1-c10)
          
          Sometimes you just want to plug a constant into a control signal.
          I give you 10 constants numbered from 1 to 10.
          
          + output: Cn
          + Parameter:a floating value
            
   
   Beside these objects, there are more general settings which should be
   adjusted:
   
   Trigger:
          
          The trigger provides timing for all the envelope generators.
          
          + Output: (internally used by all Envelope Generators)
          + Parameter: On time (Trig_on), Off time (Trig_Off),
            Repeat (Trig_Rep)
            
          
   Duration:
          
          The duration controls how long the sample will end up being, in
          seconds.
          
          + Parameter: Duration (duration)
            
          
   Output Format:
          
          The synthesizer can return a mu-law encoded sample (Au), which is
          8 bits mono at 8012 Hz, or a NeXT/Sun snd file(snd), which is 16
          bit mono at 22050 Hz.
          
          + Parameter: format (format) [ mu-law (Au), NeXT/Sun (snd)]
   Version:
          The "version" of the sinth control file can be explicitly set.
          Otherwise, it will assume the modt current version.

          + Parameter: version (floating point number)


Additional Notes:
 - All sounds are computed in floating point and scaled and converted to
   whatever the output format may be. Thus, envelopes and other scaling
   can be pretty sloppy.
 - the command order is irrelevant, with the exception that only the last
   setting of a bunch of duplicated parameter settings will be used.
 - If several sources are routed to a single control, they will be summed!
 - Sinth gives lots of error messages, with offending line numbers.
 - Sinth cannot violate the laws of physics, so keep your frequencies below
   nyquist, please (i.e. <4KHz for .au, 11KHz for snd). You can alias,
   though, if you want to.
 - Some things may change in the future: don't expect old command files to
   work in the next release, although they probably will.


Here is a typical bunch of example patches:

1: ultra simple patch:
  # this is the simplest patch!
  # because of defaults, this will produce a 110 Hz sinewave 1 second long
  # with no envelope, 
  out=o1

2: the same with all parameters fleshed out minimally
  # more detailed
  #  plug the first oscillator in out.
  out=o1
  # more about the oscillator:
  o1f=c1; C1=110.0  # use C1 to set frequency
  o1w=Sine # set up waveform type
  o1Fs=Hertz # set up frequency type
  o1A=c2; c2=1.0  # use C2 for amplitude
  # use C3 for Duty Cycle
  o1d=C3; C3=1.0 
  # set the gate's envelope signal to 1.0, in c4
  g1e=c4; C4=1.0
  # foramts and triggers
  format=au
  trig_on=0.37; trig_off=0.17; trig_rep=0
  duration=0.5
  # See why we use those defaults????


3: more fun! an enveloped filtered noise
  Version=1.0 # optional version
  duration=2.0 # 2 secs of noise
  trig_on=1    # one second on,
  trig_off=0.37 # .37 sec off
  trig_rep=10  # repeat for a while

  #the envelope (plugs into the frequency of the filter)
  e1l=10
  e1ar=2
  e1al=2000
  e1dr=4
  e1sl=1000
  e1rr=4
  e1rl=10

  out=f1   # we hear the output of the filter

  # filter
  f1s=n1    # the source is "pure" noise
  f1f=eg1   # the envelope goes into the frequency
  f1q=c1;c1=10    # filter resonance is "C1", which is 10

4: sum of sines!
  # sum these sines!
  out=o1
  out=o2
  out=o3
  #
  o1f=c1;c1=100
  o2f=c2;c2=104
  o3f=c3;c3=700
  duration=1.0

5: ring modulated (AM)

  o1f=c1;c1=200
  o2f=c2;c2=31
  o2a=eg1 # modulation index will be enveloped!
  e1l=0
  e1ar=2
  e1al=0.5
  e1dr=4
  e1sl=0.25
  e1rr=4
  e1rl=0

  g1s=o1
  g1e=o2  # a gate is also a ring modulator!

  out=g1 # take output from gate1

  duration=1.0

6: FM
  
  out=o1	# o1 is the carrier
  o1f=o2	# o2 is the modulator
  o1f=c1;c1=200 # (add o2's signal to 200 Hz!)
  o2f=c2;c2=11 # run o2 at a low frequency
  o2a=eg1 # modulation index will be enveloped!
  e1l=0
  e1ar=2
  e1al=50
  e1dr=4
  e1sl=20
  e1rr=4
  e1rl=0
  duration=1.0

7:  duty mod/filter fun!
out=f1

o1f=c1;c1=190
o1d=o2;
o1w=triangle

o2f=c2;c2=5
o2a=c3;c3=0.50

f1s=o1
f1f=eg1
f1q=c4;c4=4

e1l=10
e1al=2000
e1sl=500
e1rl=10

e1ar=5
e1dr=2
e1rr=2

duration=2.0
trig_on=1.0
trig_off=1.0

8: #sequencer fun!
duration=2.4

sq1A=110
sq1B=137.5
sq1C=165
sq1D=220
sq1E=385.0
sq1F=330.0
sq1G=440.0
sq1H=165.0

sq1s=0.15
trig_rep=100
trig_on=0.2
trig_off=0.1

e1l=0
e1ar=10
e1al=1
e1dr=15
e1sl=0.25
e1rr=10
e1rl=0

o1f=sq1
o1w=triangle
o1a=eg1
out=o1



Get the idea?

INTERNET SYNTHESIZER:
 You can drive this program from an HTML form and cgi perl script
 combo!  Just change the pathnames in all the the perl scripts
 "sinth*.pl" to point to the proper directories and install it in
 the server's cgi-bin directory. You should also fix up the URL
 that the form points to in sinth_mods.html and the other synthesis
 html pages.

VERSION INFO:
V 0.10 was the original release
V 0.11 fixed bugs in the filter and a few other places.
       added the sequencer and output options and generalized the internals.
       The html pages were also streamlined somewhat.
V 0.12 fixed a bug in the envelope generator and added more html/perl combos.

INSTALLATION NOTE for sinth:
  The Makefile may need to be adapted to accomodate Intel-ordered
bytes. Just set the compilation flag "-DIBM". I bet you can write a better
Makefile than I can anyway. Please do and send it to me! 

THIS SOFTWARE IS COPYRIGHT 1995/1996 HENRY LOWENGARD, jhhl@panix.com.
OF COURSE, THIS IS FREEWARE AND I CANNOT BE HELD RESPONSIBLE FOR DAMAGES
DONE TO YOUR COMPUTER BY THIS PROGRAM, WHATEVER THEY MAY BE. SHOULD YOU WISH
TO REDISTRIBUTE THIS, PLEASE KEEP THE SOURCE CODE AND AUXILIARY FILES WITH
IT. I'D LIKE TO HAVE A COPY OF ANY CHANGES YOU MAY MAKE, SINCE I CAN'T
TEST THIS ON A LOT OF PLATFORMS AND REALLY DON'T KNOW A HECK OF A LOT
ABOUT C, "THE LANGUAGE OF THE PHONE COMPANY."

 Future enhancements:
 - Dynamically allocated constants.
 - Dynamically allocated modules.
 - more interesting modules.
 - other HTML interfaces.